## Slide 1: Investigation of Mining Induced Ground Stress Evolution and Its Effect on Ground Stability
PACA Underground Stone Conference
October 6, 2022

## Slide 2: Outline
Research Motivation
Background Pennsy Supply, Thomasville Mine
Field Monitoring & Data Collection
Data Analysis
Conclusions

## Slide 3: Research Motivation
Large open mines produce aggregate and other industrial minerals for use in wide range of consumer products/infrastructure
Ground control vital aspect of safe/productive mines
Pillar design theories use Factor of Safety
Mine-induced stresses not well understood
Recent massive pillar collapses highlight need for in-depth studies

## Slide 4: Background - Geology
  General Geology
  Lower Cambrian Age
  Kinzer Formation – Thomasville Member
    Characterized as Limestone, Marble & Breccia
  Broad Anticline NE to SW
  Several Contacts
      Triassic - Ledgers
      Phyllite

## Slide 5: Background - Geology
Stratigraphy
  Bedded Units
  Marker Beds
Unique to Thomasville Member
Cross faults prevalent throughout deposit

## Slide 6: Background – Mine Layout

## Slide 7: Background – Mine Blasting Procedures
Room and Pillar
  Extraction via Drill/Blast
74 Hole V Cut Pattern
2” Holes
MS Delays
  8-12 holes per delay
Bulk Product
  22.5lbs/ hole Emulsion
  15lbs/ hole ANFO

## Slide 8: Field Monitoring & Data Collection
Strain Gauges
  Geokon 4360
Seismographs
  MultiSeis Plus Geophones
Data Loggers
  Ability to Capture Static and Dynamic strain
Dynamic Monitoring
  Triggered by blast event
Static Monitoring
  Min, Max and Average in varying intervals

## Slide 9: Field Monitoring & Data Collection
Lower Mine 2
  90% of Production
Strategically located to maximize recordings
6 Strain Sensors Total
  Oriented at 0, 60 and 120 degrees to measure strain changes in each plane
1 Geophone
  Trigger at 0.05 inches/second Velocity
2 Data Collectors

## Slide 10: Field Monitoring & Data Collection
Weekly Data Collection
  CR8 – Laser, Temp, RH
  CR6 – Static and Dynamic Strain Data
Battery Powered

## Slide 11: Data Analysis

## Slide 12: Data Analysis

## Slide 13: Data Analysis
Attenuation Studies
Vibration Attenuation
Vibration Attenuation Each Plane
Attenuation of Dynamic Movement Roof and Pillar Boreholes
Correlation Borehole Dynamic Movement and Particle Velocity in Pillar
Small scatter of data
Maximum Particle Velocity – Horizontal Plane
Positive Correlation between PV and borehole dynamic movement

## Slide 14: Data Analysis
Static Change – 1 month
Circles proportional to size of blast – lower SD = Large Circle
Upward movement represents expansion, downward movement shrinkage
Borehole response directly related to SD of blast.

## Slide 15: Data Analysis

## Slide 16: Conclusions
PPV attenuates as expected with SD
Peak Vector Sum likely to happen within detonation of interior holes
Correlation between SD and sudden changes
Horizontal PPV almost greater by factor of 2.2

## Slide 17: Thank You! Questions?